## Slide 1
GPU Parallel Computing
Zehuan Wang HPC Developer Technology Engineer

## Slide 2: Access The Power of GPU
Application
Library
Language
Matlab, AutoCAD, LAMMPS….
cuFFT, cuBLAS, cuSPARSE, OpenCV..
CUDA C/C++, OpenACC, CUDA Fortran, Python

## Slide 3: Access The Power of GPU
Applications
Libraries
Programming Languages
OpenACC Directives

## Slide 4
NVIDIA cuFFT
NVIDIA cuSPARSE
GPU Accelerated Libraries “Drop-in” Acceleration for your Applications
NVIDIA cuBLAS
NVIDIA cuRAND
NVIDIA NPP
Vector Signal Image Processing
Matrix Algebra on GPU and Multicore
C++ Templated Parallel Algorithms
IMSL Library
GPU Accelerated
Linear Algebra
Building-block Algorithms
CenterSpace NMath
Notes: S3461A - CUDA Accelerated Compute Libraries (Maxim Naumov: new features, how to use)
Monday, 10:30am in 210H
Monday, 2:30pm in 212A
There are a wide variety of computational libraries available.
You are probably familiar with the FFTW Fast Fourier Transform library, the various BLAS linear algebra libraries, Intel’s Math Kernel Library and Integrated Performance Primitives libraries, to name a few.
But what you might not know is that there are compatible GPU-accelerated libraries available as drop-in replacements for all of these libraries, and many more.
Including both open source and commercially supported libraries.
e.g. IMSL – International Mathematics & Statistics Library
GPU-accelerated libraries are the most straightforward way to add GPU acceleration to applications, and in many cases their performance cannot be beat.
Background:
* cuBLAS is NVIDIA’s GPU-accelerated BLAS linear algebra library, which includes very fast dense matrix and vector computations.
* cuSPARSE is NVIDIA’s Sparse matrix library, which includes sparse matrix-vector multiplication, fast sparse linear equation solvers, and tridiagonal solvers.
* NVIDIA Performance Primitives (NPP) includes literally thousands of signal and image processing functions.
* cuFFT is NVIDIA’s GPU-accelerated Fast Fourier Transform Library.
* cuRAND is NVIDIA’s GPU-accelerated random number generation library, which is useful in Monte Carlo algorithms and financial applications, among others.
* Thrust is an open-source C++ Template library of parallel algorithms such as sorting, reductions, searching, and set operations.
All are FREE and included in the CUDA Toolkit, available at www.nvidia.com/getcuda

## Slide 5: GPU Programming Languages
OpenACC, CUDA Fortran
Fortran
OpenACC, CUDA C
C
CUDA C++, Thrust, Hemi, ArrayFire
C++
Anaconda Accelerate, PyCUDA, Copperhead
Python
MATLAB, Mathematica, LabVIEW
Numerical analytics
developer.nvidia.com/language-solutions
CUDAfy.NET, Alea.cuBase
.NET
Notes: Doesn’t show Java, or the growing list of DSLs being developed to address domain-specific challenges in many fields.
GTC Dinner with Strangers last night and met Phil Pratt-Szeliga, who created the Rootbeer compiler for running Java code on GPUs.
S3058 - Rootbeer: Seamlessly Using GPUs from Java (Phil Pratt-Szeliga, Syracuse)
Wednesday, 9:30am in 231
That covers the Libraries, OpenACC Directives and Programming Language solutions… the 3 approaches to accelerating your applications.

## Slide 6: GPU Architecture

## Slide 7: GPU: Massively Parallel Coprocessor
A GPU is
  Coprocessor to the CPU or Host
  Has its own DRAM
  Runs 1000s of threads in parallel
  Single Precision: 8.74TFlop/s （k80）
  Double Precision: 2.91TFlop/s

## Slide 8: Heterogeneous Parallel Computing
Latency-Optimized
Fast Serial Processing
Logic()
Compute()

## Slide 9: Heterogeneous Parallel Computing
Latency-Optimized
Fast Serial Processing
Throughput-Optimized
Fast Parallel Processing
Logic()
Compute()
Notes: CPU是针对穿行程序对延迟进行优化的处理器。

## Slide 10: Heterogeneous Parallel Computing
Latency-Optimized
Fast Serial Processing
Throughput-Optimized
Fast Parallel Processing
Logic()
Compute()

## Slide 11: GPU in Computer System
Connected to CPU chipset by PCIe
16GB/s One Way, 32GB/s in both way
PCIe
CPU
DRAM
DDR3

## Slide 12: GPU High Level View
Streaming Multiprocessor (SM)
  A set of CUDA cores
Global memory

## Slide 13: Basic Concepts
PCI Bus
Transfer data
Offload computation
GPU
GPU Memory
CPU
CPU Memory
GPU computing is all about 2 things:
Transfer data between CPU-GPU
Do parallel computing on GPU
Notes: !这样的硬件设计也导致了，我们的GPU程序可以分为两个部分。

## Slide 14: GPU Programming Basics

## Slide 15: How To Get Start
CUDA C/C++: download CUDA drivers & compilers & samples free from:
http://developer.nvidia.com/cuda/cuda-downloads
CUDA Fortran: PGI
OpenACC: PGI, CAPS, Cray

## Slide 16: CUDA Programming Basics
Hello World
  Basic syntax, compile & run
GPU memory management
  Malloc/free
  memcpy
Writing parallel kernels
  Threads & block
  Memory hierarchy

## Slide 17: Heterogeneous Computing
Executes on both CPU & GPU
  Similar to OpenMP’s fork-join pattern
Accelerated kernels
  CUDA: simple extensions to C/C++
Device
Grid 0
Block (2, 1)
Block (1, 1)
Block (0, 1)
Block (2, 0)
Block (1, 0)
Block (0, 0)
Host
C Program Sequential Execution
Serial code
Parallel kernel
Kernel0<<<>>>()
Serial code
Parallel kernel
Kernel1<<<>>>()
Host
Device
Grid 1
Block (1, 1)
Block (1, 0)
Block (1, 2)
Block (0, 1)
Block (0, 0)
Block (0, 2)

## Slide 18: Hello World on CPU
hello_world.c:
#include <stdio.h>
void hello_world_kernel() {
printf(“Hello World\n”);
}
int main() { hello_world_kernel(); }
Compile & Run:
gcc hello_world.c
./a.out

## Slide 19: Hello World on GPU
hello_world.cu:
#include <stdio.h>
__global__ void hello_world_kernel() {
printf(“Hello World\n”);
}
int main() { hello_world_kernel<<<1,1>>>(); }
Compile & Run:
nvcc hello_world.cu
./a.out

## Slide 20: Hello World on GPU
CUDA kernel within .cu files
.cu files compiled by nvcc
CUDA kernels preceded by “__global__”
CUDA kernels launched with “<<<…,…>>>”
hello_world.cu:
#include <stdio.h>
__global__ void hello_world_kernel() {
printf(“Hello World\n”);
}
int main() { hello_world_kernel<<<1,1>>>(); }
Compile & Run:
nvcc hello_world.cu
./a.out

## Slide 21: Memory Spaces
CPU and GPU have separate memory spaces
  Data is moved across PCIe bus
Use functions to allocate/set/copy memory on GPU
  Very similar to corresponding C functions

## Slide 22: CUDA C/C++ Memory Allocation / Release
Host (CPU) manages device (GPU) memory:
  cudaMalloc (void ** pointer, size_t nbytes)
  cudaMemset (void * pointer, int value, size_t count)
  cudaFree (void* pointer)
  int nbytes = 1024*sizeof(int);
  int * d_a = 0;
  cudaMalloc( (void**)&d_a, nbytes );
  cudaMemset( d_a, 0, nbytes);
  cudaFree(d_a);

## Slide 23: Data Copies
cudaMemcpy( void *dst, void *src, size_t nbytes, enum cudaMemcpyKind direction);
  returns after the copy is complete
  blocks CPU thread until all bytes have been copied
  doesn’t start copying until previous CUDA calls complete
enum cudaMemcpyKind
  cudaMemcpyHostToDevice
  cudaMemcpyDeviceToHost
  cudaMemcpyDeviceToDevice
Non-blocking memcopies are provided

## Slide 24: Code Walkthrough 1
Allocate CPU memory for n integers
Allocate GPU memory for n integers
Initialize GPU memory to 0s
Copy from GPU to CPU
Print the values

## Slide 25: Code Walkthrough 1
#include <stdio.h>
int main()
{
int dimx = 16;
int num_bytes = dimx*sizeof(int);
int *d_a=0, *h_a=0; // device and host pointers

## Slide 26: Code Walkthrough 1
#include <stdio.h>
int main()
{
int dimx = 16;
int num_bytes = dimx*sizeof(int);
int *d_a=0, *h_a=0; // device and host pointers
h_a = (int*)malloc(num_bytes);
cudaMalloc( (void**)&d_a, num_bytes );

## Slide 27: Code Walkthrough 1
#include <stdio.h>
int main()
{
int dimx = 16;
int num_bytes = dimx*sizeof(int);
int *d_a=0, *h_a=0; // device and host pointers
h_a = (int*)malloc(num_bytes);
cudaMalloc( (void**)&d_a, num_bytes );
cudaMemset( d_a, 0, num_bytes );
cudaMemcpy( h_a, d_a, num_bytes, cudaMemcpyDeviceToHost );

## Slide 28: Code Walkthrough 1
#include <stdio.h>
int main()
{
int dimx = 16;
int num_bytes = dimx*sizeof(int);
int *d_a=0, *h_a=0; // device and host pointers
h_a = (int*)malloc(num_bytes);
cudaMalloc( (void**)&d_a, num_bytes );
cudaMemset( d_a, 0, num_bytes );
cudaMemcpy( h_a, d_a, num_bytes, cudaMemcpyDeviceToHost );
for(int i=0; i<dimx; i++)
printf("%d ", h_a[i] );
printf("\n");
free( h_a );
cudaFree( d_a );
return 0;
}

## Slide 29: Compile & Run
nvcc main.cu
./a.out
  0000000000000000
Notes: 编译

## Slide 30: Thread Hierarchy
2-level hierarchy: blocks and grid
  Block = a group of up to 1024 threads
  Grid = all blocks for a given kernel launch
  E.g. total 72 threads
    blockDim=12, gridDim=6
A block can:
  Synchronize their execution
  Communicate via shared memory
Size of grid and blocks are specified during kernel launch
  dim3 grid(6,1,1), block(12,1,1); kernel<<<grid, block>>>(…);
Grid 0
Block (2, 1)
Block (1, 1)
Block (0, 1)
Block (2, 0)
Block (1, 0)
Block (0,0)
Notes: 不是，而是，假设block中有12个线程
像我们这个例子

## Slide 31: IDs and Dimensions
Threads:
  3D IDs, unique within a block
Blocks:
  3D IDs, unique within a grid
Built-in variables:
  threadIdx: idx within a block
  blockIdx: idx within the grid
  blockDim: block dimension
  gridDim: grid dimension
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Notes: Block 1~3都支持
告诉

## Slide 32
GPU and Programming Model
Software
GPU
Threads are executed by scalar processors
Thread
CUDA Core
Thread
Block
Multiprocessor
Thread blocks are executed on multiprocessors
...
Grid
Device
A kernel is launched as a grid of thread blocks
Notes: 因为~

## Slide 33: Which thread do I belong to?
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3
threadIdx.x:
blockIdx.x:
0
0
0
0
3
3
3
3
2
2
2
2
1
1
1
1
blockDim.x = 4, gridDim.x = 4
0
1
2
3
12
13
14
15
8
9
10
11
4
5
6
7
idx = blockIdx.x*blockDim.x + threadIdx.x:

## Slide 34: Code Walkthrough 2: Simple Kernel
Build on Walkthrough 1
Write a kernel to initialize integers
Copy the result back to CPU
Print the values

## Slide 35: Kernel Code (executed on GPU)
__global__ void kernel( int *a )
{
int idx = blockIdx.x*blockDim.x + threadIdx.x;
a[idx] = 7;
}

## Slide 36
#include <stdio.h>
__global__ void kernel( int *a, int n )
{
int idx = blockIdx.x*blockDim.x + threadIdx.x; if (idx < n)
a[idx] = 7;
}
int main()
{
int dimx = 16;
int num_bytes = dimx*sizeof(int);
int *d_a=0, *h_a=0; // device and host pointers
h_a = (int*)malloc(num_bytes);
cudaMalloc( (void**)&d_a, num_bytes );
cudaMemset( d_a, 0, num_bytes );
dim3 grid, block;
block.x = 4;
grid.x = dimx / block.x;
kernel<<<grid, block>>>( d_a, dimx );
cudaMemcpy( h_a, d_a, num_bytes, cudaMemcpyDeviceToHost );
for(int i=0; i<dimx; i++)
printf("%d ", h_a[i] );
printf("\n");
free( h_a );
cudaFree( d_a );
return 0;
}

## Slide 37: Kernel Variations and Output
__global__ void kernel( int *a )
{
int idx = blockIdx.x*blockDim.x + threadIdx.x;
a[idx] = 7;
}
__global__ void kernel( int *a )
{
int idx = blockIdx.x*blockDim.x + threadIdx.x;
a[idx] = blockIdx.x;
}
__global__ void kernel( int *a )
{
int idx = blockIdx.x*blockDim.x + threadIdx.x;
a[idx] = threadIdx.x;
}
Output: 7 7 7 7 7 7 7 7 7 7 7 7 7 7 7 7
Output: 0 0 0 0 1 1 1 1 2 2 2 2 3 3 3 3
Output: 0 1 2 3 0 1 2 3 0 1 2 3 0 1 2 3

## Slide 38: CUDA Fortran
Kernels: add attributes(global) to subroutine
  Kernels should be put into a module
Same built-in variables
  threadIdx, blockIdx, blockDim, gridDim
  Now starts from 1

## Slide 39
module cuda_kernels
contains
attributes(global) subroutine kernel(a,n)
implicit none
integer, value :: n
integer :: a(n)
integer :: idx
idx = (blockIdx%x-1)*blockDim%x + threadIdx%x
if (idx .le. N) a(idx) = 7
end subroutine kernel
end module cuda_kernels
program main
use cuda_kernels
implicit none
integer, parameter :: dimx = 16 integer, allocatable :: h_a(:)
integer, allocatable, device :: d_a(:) type(dim3) grid, block
allocate(h_a(dimx))
allocate(d_a(dimx))
block=dim3(4,1,1)
grid=dim3(dimx/block%x,1,1)
call kernel<<<grid,block>>>(d_a,dimx)
h_a = d_a
print *, h_a
deallocate(h_a)
deallocate(d_a)
end program main
#include <stdio.h>
__global__ void kernel( int *a, int n )
{
int idx = blockIdx.x*blockDim.x + threadIdx.x;
if (idx < n)
a[idx] = 7;
}
int main()
{
int dimx = 16;
int num_bytes = dimx*sizeof(int);
int *d_a=0, *h_a=0; // device and host pointers
h_a = (int*)malloc(num_bytes);
cudaMalloc( (void**)&d_a, num_bytes );
cudaMemset( d_a, 0, num_bytes );
dim3 grid, block;
block.x = 4;
grid.x = dimx / block.x;
kernel<<<grid, block>>>( d_a, dimx );
cudaMemcpy( h_a, d_a, num_bytes, cudaMemcpyDeviceToHost );
for(int i=0; i<dimx; i++)
printf("%d ", h_a[i] );
printf("\n");
free( h_a );
cudaFree( d_a );
return 0;
}

## Slide 40: CUDA Fortran “cuf” directive
Similar to OpenACC, just add a directive to the loop.
!$cuf kernel do(1) <<<*,128>>> do I=1,n a(i) = a(i)+b(i) enddo

## Slide 41: GPU Memory Hierarchy: 3 Levels
Register
Cache
  L1/L2
  Shared memory
  Constant cache
  Texture cache
DRAM/Global Memory

## Slide 42: GPU Memory Model Review
Thread
Per-thread
Local
Memory
Block
Per-block Shared
Memory
Kernel 0
. . .
Per-device
Global
Memory
. . .
Kernel 1
Sequential
Kernels
Notes: 哪些存储空间对于哪些线程是可见的呢

## Slide 43: Global Memory
Kernel 0
. . .
Per-device Global
Memory
. . .
Kernel 1
Sequential
Kernels
Accessible by all threads as well as host (CPU)
Data lifetime = from allocation to deallocation

## Slide 44: Shared Memory
C/C++: __shared__ int a[SIZE]; Fortran: shared
Allocated per threadblock
Data lifetime = block lifetime
Accessible by any thread in the threadblock
  Not accessible to other threadblocks
Block
Per-block Shared
Memory
Notes: 对所对应的的block中每个线程是可见的。

## Slide 45: Registers and Local Memory
Thread
Per-thread Local Storage
Automatic variables (scalar/array) inside kernels
Spills to local memory
Data lifetime = thread lifetime

## Slide 46: Example of Using Shared Memory
Applying a 1D stencil to a 1D array of elements:
  Each output element is the sum of all elements within a radius
For example, for radius = 3, each output element is the sum of 7 input elements:
radius
radius
Notes: 是计算输入数据一定半径内所有数据之和

## Slide 47: Kernel Code Using Global Memory
__global__ void stencil(int* in, int* out) {
int globIdx = blockIdx.x * blockDim.x + threadIdx.x;
int value = 0;
for (offset = - RADIUS; offset <= RADIUS; offset++)
value += in[globIdx + offset];
out[globIdx] = value;
}
One element per thread
A lot of redundant read in neighboring threads: not an optimized way

## Slide 48: Implementation with Shared Memory
One element per thread
  Read (BLOCK_SIZE + 2 * RADIUS) elements from global memory to shared memory
  Compute BLOCK_SIZE output elements in shared memory
  Write BLOCK_SIZE output elements to global memory
“halo”
= RADIUS elements on the left
“halo”
= RADIUS elements on the right
The BLOCK_SIZE input elements corresponding to the output elements

## Slide 49: Kernel Code
__global__ void stencil(int* in, int* out) {
__shared__ int shared[BLOCK_SIZE + 2 * RADIUS];
int globIdx = blockIdx.x * blockDim.x + threadIdx.x;
int locIdx = threadIdx.x + RADIUS;
shared[locIdx] = in[globIdx];
if (threadIdx.x < RADIUS) {
shared[locIdx – RADIUS] = in[globIdx – RADIUS];
shared[locIdx + BLOCK_DIMX] = in[globIdx + BLOCK_SIZE];
}
__syncthreads();
int value = 0;
for (offset = - RADIUS; offset <= RADIUS; offset++)
value += shared[locIdx + offset];
out[globIdx] = value;
}
RADIUS = 3
BLOCK_SIZE = 16

## Slide 50: Thread Synchronization Function
void __syncthreads();
Synchronizes all threads in a thread block
  Since threads are scheduled at run-time
  Once all threads have reached this point, execution resumes normally
  Used to avoid RAW / WAR / WAW hazards when accessing shared memory
Should be used in conditional code only if the conditional is uniform across the entire thread block
  Otherwise may lead to deadlock
Notes: 当一个线程运行到

## Slide 51: Thank you
Notes: Try out OpenACC directives today. Thanks for listening, and remember: you can access all the presentations in this series by clicking the attachments link in your viewing window.